## Slide 1: Signal Processing First
Lecture 11
Linearity & Time-Invariance
Convolution

## Slide 2: License Info for SPFirst Slides
This work released under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation

## Slide 3: READING ASSIGNMENTS
This Lecture:
  Chapter 5, Sections 5-5 and 5-6
    Section 5-4 will be covered, but not “in depth”
Other Reading:
  Recitation: Ch. 5, Sects 5-6, 5-7 & 5-8
    CONVOLUTION
  Next Lecture: start Chapter 6

## Slide 4: LECTURE OBJECTIVES
  BLOCK DIAGRAM REPRESENTATION
    Components for Hardware
    Connect Simple Filters Together to Build More Complicated Systems
LTI SYSTEMS
GENERAL PROPERTIES of FILTERS
  LINEARITY
  TIME-INVARIANCE
  ==> CONVOLUTION

## Slide 5: OVERVIEW
IMPULSE RESPONSE,
  FIR case: same as
CONVOLUTION
  GENERAL:
  GENERAL CLASS of SYSTEMS
  LINEAR and TIME-INVARIANT
ALL LTI systems have h[n] & use convolution

## Slide 6: DIGITAL FILTERING
CONCENTRATE on the FILTER (DSP)
DISCRETE-TIME SIGNALS
  FUNCTIONS of n, the “time index”
  INPUT x[n]
  OUTPUT y[n]
FILTER
D-to-A
A-to-D
x(t)
y(t)
y[n]
x[n]

## Slide 7: BUILDING BLOCKS
BUILD UP COMPLICATED FILTERS
  FROM SIMPLE MODULES
  Ex: FILTER MODULE MIGHT BE 3-pt FIR
FILTER
y[n]
x[n]
FILTER
FILTER
+
+
INPUT
OUTPUT

## Slide 8: GENERAL FIR FILTER
FILTER COEFFICIENTS {bk}
  DEFINE THE FILTER
  For example,

## Slide 9: MATLAB for FIR FILTER
yy = conv(bb,xx)
  VECTOR bb contains Filter Coefficients
  DSP-First: yy = firfilt(bb,xx)
FILTER COEFFICIENTS {bk}
conv2()
for images

## Slide 10: SPECIAL INPUT SIGNALS
x[n] = SINUSOID
x[n] has only one NON-ZERO VALUE
1
n
UNIT-IMPULSE
FREQUENCY RESPONSE

## Slide 11: FIR IMPULSE RESPONSE
Convolution = Filter Definition
  Filter Coeffs = Impulse Response

## Slide 12: MATH FORMULA for h[n]
Use SHIFTED IMPULSES to write h[n]
1
n
–1
2
0
4

## Slide 13: LTI: Convolution Sum
Output = Convolution of x[n] & h[n]
  NOTATION:
  Here is the FIR case:
FINITE LIMITS
FINITE LIMITS
Same as bk

## Slide 14: CONVOLUTION Example

## Slide 15: GENERAL FIR FILTER
SLIDE a Length-L WINDOW over x[n]
x[n]
x[n-M]

## Slide 16: DCONVDEMO: MATLAB GUI

## Slide 17: POP QUIZ
FIR Filter is “FIRST DIFFERENCE”
  y[n] = x[n] - x[n-1]
INPUT is “UNIT STEP”
Find y[n]

## Slide 18: HARDWARE STRUCTURES
INTERNAL STRUCTURE of “FILTER”
  WHAT COMPONENTS ARE NEEDED?
  HOW DO WE “HOOK” THEM TOGETHER?
SIGNAL FLOW GRAPH NOTATION
FILTER
y[n]
x[n]

## Slide 19: HARDWARE ATOMS
Add, Multiply & Store

## Slide 20: FIR STRUCTURE
Direct Form
SIGNAL
FLOW GRAPH

## Slide 21: Moore’s Law for TI DSPs
Double every
18 months ?
LOG SCALE

## Slide 22: SYSTEM PROPERTIES
MATHEMATICAL DESCRIPTION
TIME-INVARIANCE
LINEARITY
CAUSALITY
  “No output prior to input”
SYSTEM
y[n]
x[n]

## Slide 23: TIME-INVARIANCE
IDEA:
  “Time-Shifting the input will cause the same time-shift in the output”
EQUIVALENTLY,
  We can prove that
    The time origin (n=0) is picked arbitrary

## Slide 24: TESTING Time-Invariance

## Slide 25: LINEAR SYSTEM
LINEARITY = Two Properties
SCALING
  “Doubling x[n] will double y[n]”
SUPERPOSITION:
  “Adding two inputs gives an output that is the sum of the individual outputs”

## Slide 26: TESTING LINEARITY

## Slide 27: LTI SYSTEMS
LTI: Linear & Time-Invariant
COMPLETELY CHARACTERIZED by:
  IMPULSE RESPONSE h[n]
  CONVOLUTION: y[n] = x[n]*h[n]
    The “rule”defining the system can ALWAYS be re-written as convolution
FIR Example: h[n] is same as bk

## Slide 28: POP QUIZ
FIR Filter is “FIRST DIFFERENCE”
  y[n] = x[n] - x[n -1]
Write output as a convolution
  Need impulse response
  Then, another way to compute the output:

## Slide 29: CASCADE SYSTEMS
Does the order of S1 & S2 matter?
  NO, LTI SYSTEMS can be rearranged !!!
  WHAT ARE THE FILTER COEFFS? {bk}
S1
S2

## Slide 30: CASCADE EQUIVALENT
  Find “overall” h[n] for a cascade ?
S1
S2
S1
S2

## Slide 31: CONVOLUTION Example