## Slide 1: Signal Processing First
Lecture 12
Frequency Response
of FIR Filters

## Slide 2: License Info for SPFirst Slides
This work released under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation

## Slide 3: READING ASSIGNMENTS
This Lecture:
  Chapter 6, Sections 6-1, 6-2, 6-3, 6-4, & 6-5
Other Reading:
  Recitation: Chapter 6
    FREQUENCY RESPONSE EXAMPLES
  Next Lecture: Chap. 6, Sects. 6-6, 6-7 & 6-8

## Slide 4: LECTURE OBJECTIVES
SINUSOIDAL INPUT SIGNAL
  DETERMINE the FIR FILTER OUTPUT
FREQUENCY RESPONSE of FIR
  PLOTTING vs. Frequency
  MAGNITUDE vs. Freq
  PHASE vs. Freq
MAG
PHASE

## Slide 5: DOMAINS: Time & Frequency
Time-Domain: “n” = time
  x[n] discrete-time signal
  x(t) continuous-time signal
Frequency Domain (sum of sinusoids)
  Spectrum vs. f (Hz)
      ANALOG vs. DIGITAL
  Spectrum vs. omega-hat
Move back and forth QUICKLY

## Slide 6: LTI SYSTEMS
LTI: Linear & Time-Invariant
COMPLETELY CHARACTERIZED by:
  IMPULSE RESPONSE h[n]
  CONVOLUTION: y[n] = x[n]*h[n]
    The “rule”defining the system can ALWAYS be re-written as convolution
FIR Example: h[n] is same as bk

## Slide 7: POP QUIZ
FIR Filter is “FIRST DIFFERENCE”
  y[n] = x[n] - x[n-1]
Write output as a convolution
  Need impulse response
  Then, another way to compute the output:

## Slide 8: DIGITAL “FILTERING”
CONCENTRATE on the SPECTRUM
SINUSOIDAL INPUT
  INPUT x[n] = SUM of SINUSOIDS
  Then, OUTPUT y[n] = SUM of SINUSOIDS
FILTER
D-to-A
A-to-D
x(t)
y(t)
y[n]
x[n]

## Slide 9: FILTERING EXAMPLE
7-point AVERAGER
  Removes cosine
    By making its amplitude (A) smaller
3-point AVERAGER
  Changes A slightly

## Slide 10: 3-pt AVG EXAMPLE
USE PAST VALUES

## Slide 11: 7-pt FIR EXAMPLE (AVG)
CAUSAL: Use Previous
LONGER OUTPUT

## Slide 12: SINUSOIDAL RESPONSE
INPUT: x[n] = SINUSOID
OUTPUT: y[n] will also be a SINUSOID
  Different Amplitude and Phase
  SAME Frequency
AMPLITUDE & PHASE CHANGE
  Called the FREQUENCY RESPONSE

## Slide 13: DCONVDEMO: MATLAB GUI

## Slide 14: COMPLEX EXPONENTIAL
FIR DIFFERENCE EQUATION
x[n] is the input signal—a complex exponential

## Slide 15: COMPLEX EXP OUTPUT
Use the FIR “Difference Equation”

## Slide 16: FREQUENCY RESPONSE
Complex-valued formula
  Has MAGNITUDE vs. frequency
  And PHASE vs. frequency
Notation:
FREQUENCY
RESPONSE
At each frequency, we can DEFINE

## Slide 17: EXAMPLE 6.1
EXPLOIT
SYMMETRY

## Slide 18: PLOT of FREQ RESPONSE
RESPONSE at /3

## Slide 19: EXAMPLE 6.2
y[n]
x[n]

## Slide 20: EXAMPLE 6.2 (answer)

## Slide 21: EXAMPLE: COSINE INPUT
y[n]
x[n]

## Slide 22: EX: COSINE INPUT
Use
Linearity

## Slide 23: EX: COSINE INPUT (ans-2)

## Slide 24: MATLAB: FREQUENCY RESPONSE
HH = freqz(bb,1,ww)
  VECTOR bb contains Filter Coefficients
  SP-First: HH = freekz(bb,1,ww)
FILTER COEFFICIENTS {bk}

## Slide 25: LTI SYSTEMS
LTI: Linear & Time-Invariant
COMPLETELY CHARACTERIZED by:
  FREQUENCY RESPONSE, or
  IMPULSE RESPONSE h[n]
Sinusoid IN -----> Sinusoid OUT
  At the SAME Frequency

## Slide 26: Time & Frequency Relation
Get Frequency Response from h[n]
  Here is the FIR case:
IMPULSE RESPONSE

## Slide 27: BLOCK DIAGRAMS
Equivalent Representations
y[n]
x[n]
y[n]
x[n]

## Slide 28: UNIT-DELAY SYSTEM
y[n]
x[n]
y[n]
x[n]

## Slide 29: FIRST DIFFERENCE SYSTEM
y[n]
x[n]
y[n]
x[n]

## Slide 30: DLTI Demo with Sinusoids
FILTER
x[n]
y[n]

## Slide 31: CASCADE SYSTEMS
Does the order of S1 & S2 matter?
  NO, LTI SYSTEMS can be rearranged !!!
  WHAT ARE THE FILTER COEFFS? {bk}
  WHAT is the overall FREQUENCY RESPONSE ?
S1
S2

## Slide 32: CASCADE EQUIVALENT
MULTIPLY the Frequency Responses
y[n]
x[n]
x[n]
y[n]
EQUIVALENT
SYSTEM