## Slide 1: Multi-Robot Coordination Using a Market-based Approach

## Slide 2: Outline
Why multiple robots?
Design requirements
Other approaches
The market-based approach
Example: Multi-robot exploration

## Slide 3: Why Multiple Robots?
Some tasks require a team
  Robotic soccer
Some tasks can be decomposed and divided for efficiency
  Mapping a large area, Searching landmines
Many specialists preferable to one generalist
More effective localization by exchanging info
Increase robustness with redundancy
Teams of robots allow for more varied and creative solutions
The Robotics Institute, Carnegie Mellon University

## Slide 4: A Few Multi-robot Scenarios
Automated warehouse management
Exploration and colonization of hazardous environments (planetary, disaster, minefield).
Automatic construction
Robotic cleanup of hazardous sites
Agriculture

## Slide 5: Outline
Why multiple robots?
Design requirements
Other approaches
The market-based approach
Example: Multi-robot exploration

## Slide 6: A Good Multi-robot System Is:
Robust: no single point of failure
Optimized, even under dynamic conditions
Quick to respond to changes
Able to deal with imperfect communication
Able to allocate limited resources : optimized resource utilization
Heterogeneous and able to make use of different robot skills

## Slide 7: Outline
Why multiple robots?
Design requirements
Other approaches
The market-based approach
Example: Multi-robot exploration

## Slide 8: Difficulty
Increased number of robots
Th requirement of working together
Dynamic environments
Malfunctionning robots

## Slide 9: Basic Approaches
Centralized
  Attempting optimal plans
Distributed
  Every man for himself
Market-based

## Slide 10: Centralized Approaches
Robot team treated as a single “system”
with many degrees of freedom
A single robot or central computer is the “leader”
Leader plans optimal actions for the entire group
Group members send information to leader and carry out actions

## Slide 11: Centralized Methods: Pros
Leader can take all relevant information
into account
In theory, coordination can be perfect:
  Optimal plans possible!

## Slide 12: Centralized Methods: Cons
Computationally hard
  Best known algorithms exponential in complexity
  Intractable for more than a few robots
Makes unrealistic assumptions:
  All relevant info can be transmitted to leader
  This info doesn’t change during plan construction
Result: slow or inaccurate response
Vulnerable to malfunction of leader
  Leader selection algorithm required
Heavy communication load

## Slide 13: Distributed Approaches
Planning responsibility spread over team
Each robot basically independent
Robots use locally observable information to make their plans

## Slide 14: Distributed Methods: Pros
Fast response to dynamic conditions
Little or no communication required
Little computation required
  Divide a problem into subtask
Smooth response to environmental changes
Very robust
  No single point of failure

## Slide 15: Distributed Methods: Cons
Works best for sub-task decomposable
problems, Not all problems can be decomposed well
Plans based only on local information
Result: solutions are often highly sub-optimal
because they are based on local information

## Slide 16: Outline
Why multiple robots?
Design requirements
Other approaches
The market-based approach
Example: Multi-robot exploration

## Slide 17: Market-based Approach: The Basic Idea
Based on the economic model of a free
market
Each robot seeks to maximize individual “profit”
Robots can negotiate and bid for tasks
Individual profit helps the common good
Decisions are made locally but effects approach optimality
  Preserves advantages of distributed approach

## Slide 18: Analogy To Real Economy
Robots must be self-interested
Sometimes robots cooperate
  To achieve a greater consequence
sometimes they compete
  Provide goods at lower cost, eliminating inefficiencies
Individuals reap benefits of their good decisions, suffer consequences of bad ones
Just like a real market economy, the result is global efficiency

## Slide 19: The Market Mechanism In Detail: Background
Consider:
  A team of robots assembled to perform a particular set of tasks
  Each robot is a self-interested agent
  The team of robots is an economy
  The goal is to complete the tasks while minimizing overall costs, since each robot aim to minimize its individual cost

## Slide 20: How Do We Determine Profit?
Profit = Revenue – Cost
Revnue and cost reflect nature of application domain
  Priorities on task completion
  Hard deadlines
  Acceptable margins for errors
  ...
Team revenue is sum of individual revenues, and team cost is sum of individual costs
Costs and revenues set up per application
  Maximizing individual profits must move team towards globally optimal solution
Robots that produce a lot at low cost receive a larger share of the overall profit

## Slide 21: Examples
Cost functions may be complex
  Based on distance traveled
  Based on time taken
  Some function of fuel expended, CPU cycles, etc.
Revenue based on completion of tasks
  Reaching a goal location
  Moving an object
  Etc.

## Slide 22: Prices and Bidding
Robots can receive revenue from other
robots in exchange for goods or services
  Example: haulage robot
If robots can produce more profit together than apart, they should deal with each other
  If one is good at finding objects and another is good at transporting them, they can both gain

## Slide 23: No Communication

## Slide 24: Subcontracting a Task
Notes: Here, robot 2 subcontracts task B to save 150 in cost; robot 1 sees that the new route will add 110 in cost; so they negotiate a price of 130. Both robots profit, and the global task is accomplished at a lower cost. Note that robot 2 was a leader; all it did was generate and sell a plan.

## Slide 25: How Are Prices Determined?
Bidding
  Robots negotiate until price is mutually beneficial
  Note: this moves global solution towards optimum
Robots can negotiate several deals at once
Deals can potentially be multi-party
Prices determined by supply and demand
  Example: If there are a lot of haulers, they won’t be able to command a high price
  This helps distribute robots among “occupations”
NOTE : price and bid are low bandwith mechanism for communicating aggregate cost information

## Slide 26: Competition vs. Coordination
Complementary robots will cooperate
  A grasper and a transporter could offer a combined “pick up and place” service
  Result : heterogenous robot groups
Similar robots will compete
  This drives prices down
This isn’t always true:
  Subgroups of robots could compete
  Heterogenous robots could compete if task accomplished in different ways
  Similar robots could agree to segment the market
  Several grasping robots might coordinate to move a heavy objects

## Slide 27: Leaders
A robot can offer its services as a leader
A leader must convince the group that they will make more money by following its advices
A leader investigates plans for other robots
If it finds a way for other robots to coordinate to maximize profit:
  Uses this profit to bid for the services of the robots
  Keeps some profit for itself
Note that this introduces a notion of centralization
  Difficult for more than a few robots

## Slide 28: Why Is This Good?
Robust to changing conditions
  Not hierarchical
  If a robot breaks, tasks can be re-bid to others
Distributed nature allows for quick response
Only local communication necessary
Efficient resource utilization and role adoption
Advantages of distributed system with optimality approaching centralized system

## Slide 29: Outline
Why multiple robots?
Design requirements
Other approaches
The market-based approach
Example: Multi-robot exploration

## Slide 30: Multi-Robot Exploration
Goal: explore and map unknown environment
Environment may be hostile and uncertain
Communication may be difficult
Multiple robots:
  Cover more territory more quickly
  Robust if some robots fail
Attempt to minimize repeated coverage
Key: coordination
  Maximize information gain, reduce total costs

## Slide 31: Previous Work
Balch and Arkin:
  Eliminates direct communication
  No role adoption, efficient resource utilization
Latimer: can provably cover a region with minimal repeated coverage
  Very high communication requirement
  Fails if one robot fails
Chaimowicz: tightly coupled multirobot coordination
  Central agent greedily assigns tasks
  Not robust, Suboptimal, centralized, high communication
Tambe: adaptive teams
  General purpose teamwork capabilities via machine learning
  Highly adaptable but lack to reason and optimize the use of limited sources

## Slide 32: Architecture of the Market Approach
Distributed travelling salesman problem
  Each robot equipped with a map of the world
Goal to visit a set of preselected points
  Goal points to visit are the main commodity exchanged in market
For any goal square in the grid:
  Cost based on distance traveled to reach thr city
  Revenue based on negotiated price to reach the goal
    The maximum team revenue chosen as to exceed team cost
  bid = 0.9*(r-c) + c
Team profit = sum of individual profits
  When individual robots maximize profit, the whole team gains

## Slide 33: Example World

## Slide 34: Operator Algorithm
Algorithm for each self interested operator:
Anounce all cities to all robots and wait for incoming bits
Insert each incoming bid in a priority queue with the lowest bid claiming the highest priority
Assign m cities (one to each robot) starting with the highest priority bid. (Note, once a city is assigned from the priority queue, all other bids for that city and all other bids submitted by that robot are removed from the queue before making the next assignment)
Delete all bids, and call for re-bids for all remaining cities
Repeat procedure until all n cities are assigned

## Slide 35: Exploration Algorithm
Idea : “city-for-revenue deals” minimize team cost
despite increasing some robot’s cost

## Slide 36: Exploration Algorithm
Algorithm for each robot:
Generate goals (based on goal selection strategy)
If OpExec (human operator) is reachable, check with OpExec to make sure goals are new to colony
Rank goals greedily based on expected profit
Try to auction off goals to each reachable robot
  If a bid is worth more than you would profit from reaching the goal yourself (plus a markup), sell it

## Slide 37: Exploration Algorithm
Once all auctions are closed, explore highest-profit goal
Upon reaching goal, generate new goal points
  Maximum # of goal points is limited
Repeat this algorithm until map is complete

## Slide 38: Bidding Example
R1 auctions goal to R2

## Slide 39: Expected vs. Real
Robots make decisions based on expected profit
  Expected cost and revenue based on current map
Actual profit may be different
  Unforeseen obstacles may increase cost
Once real costs exceed expected costs by some margin, abandon goal
  Don’t get stuck trying for unreachable goals

## Slide 40: Goal Selection Strategies
Possible strategies:
  Randomly select points, discard if already visited
  Greedy exploration:
    Choose goal point in closest unexplored region

## Slide 41: Benefit of Prices
Low-bandwidth mechanisms for communicating aggregate information
Unlike other systems, map info doesn’t need to be communicated repeatedly for coordination

## Slide 42: Information Sharing
If an auctioneer tries to auction a goal point already covered by a bidder:
  Bidder tells auctioneer to update map
  Removes goal point
Robots can sell map information to each other
  Price negotiated based on information gained
  Reduces overlapping exploration
When needed, OpExec sends a map request to all reachable robots
  Robots respond by sending current maps
  OpExec combines the maps by adding up cell values

## Slide 43: Experimental Setup
4 or 5 robots
  Equipped with fiber optic gyroscopes
  16 ultrasonic sensors

## Slide 44: Experimental Setup
Three test environments
  Large room cluttered with obstacles
  Outdoor patio, with open areas as well as walls and tables
  Large conference room with tables and 100 people wandering around
Took between 5 and 10 minutes to map areas

## Slide 45: Conclusion
Market-based approach for multi-robot coordination is promising
  Robustness and quickness of distributed system
  Approaches optimality of centralized system
  Low communication requirements
Probably not perfect
  Cost heuristics can be inaccurate
  Much of this approach is still speculative
    Some pieces, such as leaders, may be too hard to do