## Slide 1: Multi-Robot Exploration Controlled by a Market Economy
Çetin Meriçli
Artificial Intelligence Laboratory
Department of Computer Engineering
Bogazici University
01.04.2003

## Slide 2: Outline
Multi-Robot systems
Exploration and map making
Previous Work
Proposed Approach
Conclusions

## Slide 3: Multi-Robot Systems (Pros)
Robustness (due to redundancy)
Efficiency (parallel working of robots quickens the operation)
Free from single-point failure (if system is decentralized)

## Slide 4: Multi-Robot Systems (Cons)
High communication requirement in general
If greedy assignment methods are used, convergence to a suboptimal goal is possible

## Slide 5: Exploration & Map Making
Different possible cases
  Guaranteed total coverage is necessary (landmine detection)
  Focusing on potentially interested areas with more specific detail (planetary exploration)
  Map of the environment might be needed for further purposes (i.e. by the other teammates for path planning, etc…)

## Slide 6: Previous Work on Multi-Robot Exploration & Map Making
Balch and Arkin :
  Communication is not necessary, since robots leave a physical record on the visited portions of environment.
  Advantage : Very low communication requirement
  Disadvantages : Physical trails might not be clearly recognizable, Searching for traces decreases the exploration efficiency

## Slide 7: Previous Work on Multi-Robot Exploration & Map Making (cont’d)
Latimer :
  The robots sweep the space together in a parallel line formation until they reach an obstacle. At this point, team splits up at the obstacle and can opportunistically rejoin at some later point.
  Advantage : Minimal repeated coverage
  Disadvantage : Single-point failure

## Slide 8: Previous Work on Multi-Robot Exploration & Map Making (cont’d)
Simmons :
  Known cells bordering unknown environment are called “Frontier Cells”
  Each robot evaluate a set of frontier cells (determine expected travel cost and information gain) and bid for each frontier cell. Information gain is based on estimated number of unexplored neighbor cells.
  A central agent (with a central map) greedily assigns tasks based on bids
  Disadvantages : Single-point failure, possibility of converging to suboptimal results.

## Slide 9: Previous Work on Multi-Robot Exploration & Map Making (cont’d)
Yamauchi :
  Improved frontier approach
  Robots share sensor information, so each robot has the same frontier list.
  Each robot moves to closest frontier, performs sensing and broadcasting the results
  Advantages : Fully distributed and asynchronus (no single-point failure)
  Disadvantages : Possible repeated coverage (new frontiers generally originated from old ones and discovered new frontiers are often closest frontiers. A robot moving to same original frontier will be close to the new frontier as well. This may cause to robots end up following a leader indefinitely

## Slide 10: Proposed Approach
Market Architecture
  Cost function is based on the distance information. Expected cost is the estimated distance traveled to each goal (TSP problem, NP-Hard)
  Revenue function : World is represented as an occupancy grid (Marks : free, obstacle or unknown ). Information gained by visiting a goal point is calculated by counting the number of unknown cells within a fixed neighborhood of the goal point
  Profit = revenue - cost

## Slide 11: Proposed Approach (cont’d)
Goal point selection strategies
  Random : Goal points are chosen at random, but discarded if the area surrounding the goal area has already explored
  Greedy Exploration : Select the center of closest unexplored region larger than a certain threshold as the goal point
  Space Division by Quadtree : Unknown cells are represented by using a quadtree. A region is divided into its four children if the fraction of unexplored space in the region is over a certain threshold. Subdivision stops when size of a leaf region is smaller than a sensor footprint. Goal points are centers of regions.

## Slide 12: Proposed Approach (cont’d)
Since terrain is not known in advance, some goals may not be reachable. In such case, robot is drawn towards the edge of reachable space while attempting to achieve its goal. This results in more detail in areas if the map near boundaries and walls (which are usually most interesting areas)
If the incurred travel cost exceeds initial estimated cost by a certain margin, goal is considered as unreachable and robot moves on to the next goal. This avoids indefinite trial on same unreachable goal.

## Slide 13: Proposed Approach (cont’d)
Exploration algorithm :
  Robots are initially deployed with known relative positions
  Each robot generates its own goal list
  If robot is able to communicate with OpExec, transmits the goals and checks for new ones
  Robot inserts all of the remaining goals in its current tour in a greedy fashion (shortest path)
  Robot tries to sell each of the goals to all robots who are currently able to communicate, via an auction.

## Slide 14: Proposed Approach (cont’d)
Exploration Algorithm (cont’d)
  Robot waits until all robots have bid (or a certain time is passed)
  If a robot bids more than the minimum price set by the auctioneer, the highest bidder is awarded the task in exchange for the price of the bid.
  Robot starts to navigate when all auctions are closed.

## Slide 15: Proposed Approach (cont’d)
Selling of the tasks :
  Auctioneer announces a reservation price Pr. This is the lowest possible bid auctioneer can accept.
  Remaining robots acts as buyers, negotiating to receive the right to execute the task and receive payment from the OpExec.
  Each buyer calculates its valuation for the goal by finding expected profit in adding that goal to its current tour.

## Slide 16: Proposed Approach (cont’d)
Selling of tasks (cont’d)
  Bidding strategy is defined by each buyer submitting a bid
  If bidder expects a profit greater than the reservation price, then no bid is submitted (a bid lower than reservation price can not win the auction)

## Slide 17: Proposed Approach (cont’d)
No agent ever assumes that it is connected to or able to communicate with any of the other agents. If a robot does not reveive a message it is expecting, it must be able to continue its work rather than wait for the message indefinitely. So timeout mechanism is used for avoiding this kind of deadlock
In case of a robot failure, the lost robot no longer participates in the negotiations and thus is not awarded any further tasks. The lost robot’s tasks are not completed, but other robots eventually generate goal points in the same areas.
New robots can be introduced into the colony at any time if relative position and orientation (to another robot or to a known landmark) is available.

## Slide 18: Proposed Approach (cont’d)
Information Sharing
  Aim is to reduce repeated coverage
  Any communication failures do not disable the team but reduces the efficiency of the exploration
  Robots are usually kept a reasonable distance apart from one another. If one robot has a goal point lying close to a region covered by some other robot, the other robot wins the auction since it has the lowest cost (therefore, lowest overall price). The effect is that the robots tend to stay far apart

## Slide 19: Proposed Approach (cont’d)
Information sharing (cont’d)
  If a robot (auctioneer) offers a goal that is already explored by another (bidder) robot, the bidder sends a message and informs the auctioneer of this fact so auctioneer cancels the auction and removes that point from its goal list.
  A robot may sell a portion of its knowledge about the map to another robot for a price. Price depends on the amount of new information. In case of a contradiction between a robot’s local map and received information, robot always relies on its own beliefs.

## Slide 20: Conclusion
A fully de-centralized team of robots can be developed by using market-driven approach
Immunity to communication and agent failures brings robustness.
Information changing in the market increases efficiency and decreases repeated coverage