## Slide 1: A New Planner Design for Soccer-Robots: Implementation of Potential Field Planner Using Genetic Algorithms
BY
KEMAL KAPLAN
11/02

## Slide 2: OUTLINE
Soccer Robots
System Overview
Vision and Localization
Global Vision, On-Board Vision, Localization
Locomotion
Wheeled platforms
Differential Drive Kinematics
Planner
Individual functions
Move, Defense, Attack, Goalie
Potential Field Planner
Training Potential Field Planner
Application of GA to Potential Field Planner
Results and MATCH

## Slide 3: SOCCER ROBOT SYSTEMS
Autonomous systems
Multi-agent systems
Computer vision and image processing
Intelligent control
Mechatronics
Machine learning
Robotics
Two international competitions have emerged based on this platform, FIRA and RoboCUP.

## Slide 4: SYSYEM OVERVIEW
Intelligent central controller
Dummy robots
Global vision
Wireless(RF) Communication

## Slide 5: VISION AND LOCALIZATION
Global vision: Uses an overhead camera and off-field PC to identify and track the robots as they move around the field. Usually only robot and ball colors used for identification, because of high performance requirements. Global localization is implemented by using the identified objects.
Local (On-Board) vision: Robots have their sensing on the robot itself. The vision information is either processed on-board the robot or is transmitted back to the off-field PC for processing. Relative movements are more important than exact localization

## Slide 6: LOCOMOTION
Wheeled platforms
Differential Drive
Tri-cycle Drive / Ackerman Steering
Synchro Drive
Omnidirectional Drive
Four-wheel Steering
Explicit Steering etc.

## Slide 7: DIFFERENTIAL DRIVE KINEMATICS
(t) = ∫ (t) dt
x(t) = ∫ Vx(t) dt = ∫ V(t) cos((t)) dt
y(t) = ∫ Vy(t) dt = ∫ V(t) sin((t)) dt
 = ( VR - VL ) / 2d
R = 2d ( VR + VL ) / ( VR - VL )
V = R = ( VR + VL ) / 2
Inverse Kinematics (Proportional Control):
V = kdde
 = kae
Vl = v -  (R/2) = kdde - kae (R/2)
Vl = v -  (R/2) = kdde + kae (R/2)

## Slide 8: PLANNER
Individual Functions: Base functions performed by individual robots to accomplish certain tasks. The performance of the overall system is highly dependent on those base functions.
Behavioral Functions: Functions built on individual functions to decide the action of each robot. These functions may be distributed or central depending on the overall system design.

## Slide 9: MOVE FUNCTION
Different for each locomotion system. Introduces an abstraction between planner and physical units.
Must be fast, reliable.
In our case;
  Fast: We fix speed of one of the wheels to maximum speed and calculate the other one according to that one.
  Reliable: The function is recalculated at every step. Therefore, the error is not cumulative.

## Slide 10: DEFENSE METHOD
May change according to the number of defensive players.
Must obey some constraints according to the game rules.
x_robot = (x_ball – x_homegoal) / 2
y_robot = [y_ball (y_homegoaldown + sign(defense # of robot) * goalsize / # of defense robots)] / 2

## Slide 11: ATTACK METHODS

## Slide 12: GOALIE METHOD
x/y = x’/y’

## Slide 13: POTENTIAL FIELD PLANNER
Impulsive Forces: ball, position forces
Repulsive Forces: teammates, opponents, walls, constraints

## Slide 14: POTENTIAL FUNCTIONS
1/exp (k*distance)
1/(1+exp(k* distance))
k=10 k=1 k=0.2

## Slide 15: SIMPLE FIELDS
DefenceField: Constant force to a calculated point
GoalieField: Constant force to a calculated point
PositionField: Constant force to a calculated point
OpponentField: 1/exp (k*distance) for k=1
HomeField: 1/exp (k*distance) for k=1
WallField: 1/exp (k*distance) for k=1
“distance” is the distance of the robot to the source of the potential field.
Each robot must calculate the sum of all potential fields ar each time step.

## Slide 16: BALL FIELD
There are two potential fields around the ball:
First one is a constant impulsive field,
The second one is the circular fields similar to the ones in the limit-cycle method.
The combination of these fields:
Fball = Fconstant+Fcircular/(1+exp(k* distance))

## Slide 17: POTENTIAL FILEDS AROUND LINE SEGMENTS
These potentials used to implement the constraints defined in the rules of the robot-soccer games. For example, two defense robot should not enter the goalarea at the same time therefore, we put three “line segment potential fields” around the goalarea, which prevents all the of robots, except the goalie, to enter the goalarea.

## Slide 18: ROBOT-SOCCER SIMULATORS
Mirosot Simulator:
+ Perfect Kinematic Simulation of Physical MIROSOT robots.
+ Offical simulator of the tournament
-The simulator is not open source.
- No configuration available.

## Slide 19: ROBOT-SOCCER SIMULATORS
Webots:
+ Suports VRML object definitions.
+ Entire model of the world is designed by the programmer.
Not good at robot-soccer kinematics. (next version will include necessary kinematic parameters)
Very low level implementation required.
Notes: VRML: Virtual Reality Modeling Language

## Slide 20: ROBOT-SOCCER SIMULATORS
Teambots:
+ The simulator is open source.
+ Highly configurable.
- The simulator is implemented in java which has relatively a slow virtual machine.
The kinematics of the robots are totally different than MIROSOT robots.

## Slide 21: GENETIC ALGORITHMS - BASICS
[Start] Generate random population of n chromosomes (suitable solutions for the problem)
[Fitness] Evaluate the fitness f(x) of each chromosome x in the population
[New population] Create a new population by repeating following steps until the new population is complete
  [Selection] Select two parent chromosomes from a population according to their fitness (the better fitness, the bigger chance to be selected)
  [Crossover] With a crossover probability cross over the parents to form a new offspring (children). If no crossover was performed, offspring is an exact copy of parents.
  [Mutation] With a mutation probability mutate new offspring at each locus (position in chromosome).
[Accepting] Place new offspring in a new population
[Replace] Use new generated population for a further run of algorithm
[Test] If the end condition is satisfied, stop, and return the best solution in current population
[Loop] Go to step 2
Notes: TABU SEARCH: The basic concept of Tabu Search as described by Glover (1986) is "a meta-heuristic superimposed on another heuristic. The overall approach is to avoid entrainment in cycles by forbidding or penalizing moves which take the solution, in the next iteration, to points in the solution space previously visited ( hence "tabu"). The Tabu search is fairly new, Glover attributes it's origin to about 1977 (see Glover, 1977). The method is still actively researched, and is continuing to evolve and improve. The Tabu method was partly motivated by the observation that human behavior appears to operate with a random element that leads to inconsistent behavior given similar circumstances. As Glover points out, the resulting tendency to deviate from a charted course, might be regretted as a source of error but can also prove to be source of gain. The Tabu method operates in this way with the exception that new courses are not chosen randomly. Instead the Tabu search proceeds according to the supposition that there is no point in accepting a new (poor) solution unless it is to avoid a path already investigated. This insures new regions of a problems solution space will be investigated in with the goal of avoiding local minima and ultimately finding the desired solution.
The Tabu search begins by marching to a local minima. To avoid retracing the steps used, the method records recent moves in one or more Tabu lists. The original intent of the list was not to prevent a previous move from being repeated, but rather to insure it was not reversed. The Tabu lists are historical in nature and form the Tabu search memory. The role of the memory can change as the algorithm proceeds. At initialization the goal is make a coarse examination of the solution space, known as 'diversification', but as candidate locations are identified the search is more focused to produce local optimal solutions in a process of 'intensification'. In many cases the differences between the various implementations of the Tabu method have to do with the size, variability, and adaptability of the Tabu memory to a particular problem domain.
i.e.: id est: that is

## Slide 22: GENETIC ALGORITHMS - OPERATORS
Encoding of a Chromosome: The chromosome should in some way contain information about solution which it represents. The most common encoding methods are: Binary encoding, many-character and real valued encoding, tree encoding, permutation encoding.
Crossover: Crossover selects genes from parent chromosomes and creates a new offspring. Crossover types are: One-point, two-point, uniform, arithmetic, tree crossover.
Mutation: Mutation changes randomly the new offspring, usually with a small probability. Mutation is made to prevent falling GA into local extreme, but it should not occur very often, because then GA will in fact change to random search.
Notes: permutation encoding: every chromosome is a string of numbers, which represents number in a sequence.

## Slide 23: GENETIC ALGORITHMS - PARAMETERS
Crossover probability: says how often will be crossover performed. If crossover probability is 100%, then all offspring is made by crossover. If it is 0%, whole new generation is made from exact copies of chromosomes from old population.
Mutation probability: says how often will be parts of chromosome mutated. If mutation probability is 100%, whole chromosome is changed, if it is 0%, nothing is changed.
Population size: says how many chromosomes are in population (in one generation). If there are too few chromosomes, GA have a few possibilities to perform crossover and only a small part of search space is explored. On the other hand, if there are too many chromosomes, GA slows down.

## Slide 24: GENETIC ALGORITHMS - SELECTION
Roulette Wheel Selection: Parents are selected according to their fitness. The better the chromosomes are, the more chances to be selected they have. (Stochastic Universal Sampling)
Rank Selection: Rank selection first ranks the population and then every chromosome receives fitness from this ranking.
Elitism: Elitism copies the best chromosome (or a few best chromosomes) to new population. The rest is done in classical way.
Steady-State Selection:two parents are selected to reproduce and two parents are selected to die; two offspring are immediately inserted in the pool (mammals)
Sigma Scaling: The fitness function is equivalent to the objective function minus the difference between the average performance and the standard deviation.
Boltzmann Selection: Boltzmann selection attempt to find a middle ground between these two methods. They favor rank selection in early generations and roulette selection in the latter. This is accomplished by scaling the fitness using a potential that changes over time.
Notes: The Boltzmann Factor:
Boltzmann generalized the Law of Atmospheres by interpreting the FACTOR,
e-mgy/kT
As the PROBABILITY of a given gas molecule being at the height y, in a gas of temperature T.
The Boltzmann distribution
If U = 0 is the lowest possible energy a molecule in a system can have, then in general, the PROBABILITY of a molecule having energy U in that gas at temperature T should be:
e-U/kT
So that, if there are N0 particles to begin with, only
N = N0e-U/kT
on average should have energy = U.

## Slide 25: APPLICATION OF GENETIC ALGORITHMS TO POTENTIAL FIELD PLANNER
Chromosome Encoding: The weights of the potential fields forms the chromosome.

## Slide 26: FITNESS FUNCTION AND PARAMETERS
We use Teambots to evaluate a fitness score. Each chromosome plays three matches, with different seed, against the same team. Each goal scored gives +2 fitness scrore where each goal the opponent scored gives –1 fitness score.
Parameters:
  population size: 100
  crossover probability: % 80
  random selection chance: %10
  max # of generations: 20
  chromosome mutation probability: 0.005
  crossover type: uniform

## Slide 27: RESULTS
GA start time: Sat Nov 23 13:44:48 EET 2002
GA end time: Sun Nov 24 16:16:57 EET 2002
Best Fitness: 12
Best Chromo: 3481630079489170
GA Result: 3577233539465190(7.0)
Match Count: 6660